Ballasted Polar:
with the well known equation for lift:
mg = ½ ρ S V2 Ca (1)
and
o = mb/m (2)
o = ballast overload
mb = ballasted mass
V = unballasted airspeed
S = wing area
ρ = air density constant
Ca = lift coefficient
m = unballasted mass as from reference polar
we can solve eq. (1) for V
V = sqrt( m g / ½ ρ S Ca )
as we can consider everything except mass m as constant in the above expression we can conclude:
Vb / V = sqrt( mb / m) = sqrt(o) (2)
or
V = Vb / sqrt(o) (3)
with the second order approximation for sink:
Sink (V) = a0 + a1 V + a2 V2 (4)
and (3) in (4), we get for the ballasted sink:
Sinkb (Vb/sqrt(o) ) = a0 + a1 (Vb/sqrt(o)) + a2 ( Vb/sqrt(o) ) 2
or
Sinkb (Vb) = sqrt(o) ( a0 + (a1 / sqrt(o) ) Vb + (a2 /o) Vb2 )
or, further simplified:
Sinkb (Vb) = a0 sqrt(o) + a1 Vb + (a2 / sqrt(o)) Vb2
So finally we get the polar translated for the ballasted case and thats what we do today in XCS and also XCV when user increases ballast.