Cable Overview

30 cm

   J2 FLARM

50 cm

U1

15 cm

   J1 Vario

T1

1m

S1

50 cm

Details and Wiring diagramm:
T1 (Dallas DS18B20) / Third party product: e.g. Aliexpress / 1 m cable type / „Waterproof 18B20 temperature probe temperature sensor Stainless steel package 1 meter“ / Target Price ~ 1$	S1 (Switch) / open ends / 2x AWG26 / 0,12 mm² / Ends: 5 mm stripped, soldered / Color: / 2x Black	J1 (Vario) / RJ45 connector male, 8 pin / RJ45 connector with flat or round cable 15 cm highly flexible, shielded if possible / Color: / don‘t care	U1 (Battery) / open ends / 2x 50 cm AWG23 0,25 mm² / Ends: 10mm stripped, soldered / Color: / 1 x Black / 1 x Red	J2 (FLARM) / RJ45 connector male, 8 pin / RJ45 cable with / flat or round cable 30 cm highly flexible, shielded if possible / Color: / don‘t care
		1	+12V	8
		2		7
		3		6
	1	4		5
3 (+VDD)		5		4
2 (DQ)		6		3
1 (GND)		7		2
	2	8	GND	1